## Slide 1: Making Regional Probabilistic Solar Forecasts from Deterministic Forecasts with Open-Source Tools and Data
William B. Hobbs, PE
Southern Company R&D
IEEE PVSC 2024

## Slide 2: Overview
Open-source tool to produce probabilistic forecast from an existing deterministic forecast (e.g., vendor)
Focus on day-ahead for now
Vendor PV forecast
NOAA forecasts
ML models
Historical data
(pvlib+NOAA for prototype)

## Slide 3: Motivation
Lots of good deterministic forecasts are available
None are perfect
Grid operators have increasing need for uncertainty information
Most probabilistic forecasts focus on single sites
Errors across sites are not independent  can’t simply combine site-level probabilistic forecasts

## Slide 4: Tools and data
All in python, open-source (and free) tools
pvlib for weather-to-power (forecast and synthetic actuals)
Herbie to retrieve NOAA NWPs from AWS
  A portion of this work used code generously provided by Brian Blaylock's Herbie python package (Version 2024.3.1) (https://doi.org/10.5281/zenodo.4567540)
scikit-learn (sklearn) and quantile-forest (based on sklearn, published by Zillow) for ML regression models
Forecasted weather: NOAA GEFS and HRRR
“Actual” weather: NOAA HRRR* f00
Plant specs: EIA Form 860 data**
*Started with NREL NSRDB, but found an issue with cloud detection at low sun angles. Results were mostly the same, otherwise.
** All of SOCO BA

## Slide 5: Solar Fleet
About 3700 MW in Southern Company’s Balancing Area
(Improved map by Adam Jensen)

## Slide 6: Found two interesting indicators of forecast uncertainty:
Ensemble spread for cloud cover:
  Variation in cloud cover across 30 GEFS ensemble members
    For each member, calculate average cloud cover over all solar plants, weighted by plant capacity, then calculate standard deviation of those averages across all 30 ensemble members
Spatial variation in irradiance:
  Variation of irradiance (and resulting calculated fleet power) across ~30km x 30km HRRR grid (10x10 native grid cells)
    (Max – Min)/Clear Sky

## Slide 7
Timeout!
Why not just use GEFS for 30 power scenarios and calculate probabilities from that??
Great question! A few reasons:
Ensembles are generally “underdispursed” (overconfident) for solar, i.e., what actually happens too often falls outside the range of all ensemble members
The GEFS model by itself may not be great for solar
I’m not trying to build a full forecast (hard to compete with the best vendors), I want to add probabilities to an existing good forecast

## Slide 8: Cloud Cover Uncertainty Examples:
Uncertainty:
LOW

## Slide 9: Cloud Cover Uncertainty Examples:
Uncertainty:
High

## Slide 10: Cloud Cover Uncertainty Examples:
Uncertainty:
Low/Medium

## Slide 11: Real examples:
Low solar, low uncertainty day
(4 ensemble members shown, full analysis includes all 30 members)

## Slide 16: Real examples:
Low solar, high uncertainty day
(4 ensemble members shown, full analysis includes all 30 members)

## Slide 21: Real examples:
High solar, low uncertainty day
(4 ensemble members shown, full analysis includes all 30 members)

## Slide 26: Spatial variation from HRRR
Use NOAA’s HRRR (high resolution rapid refresh) model

## Slide 33
Max
Min
…model power, repeat for all plants, sum mins, sum maxes

## Slide 34: Example results:
High uncertainty
Low uncertainty
Medium uncertainty

## Slide 35: TCC and spatial variation for the days we’ve been looking at:

## Slide 36: …now in a scatter plot:

## Slide 37: … and for 2 full years:
My conclusion: There’s something there, but it’s not a clear relationship

## Slide 38: Solution:
Machine learning quantile regression models: Random Forest, XGBoost
Inputs:
  Existing forecast (normalized)
  Historical forecast error (normalized)
  Std. of TCC
  HRRR “spread”
  Position of the sun in the sky
  Month of year
Output:
  Updated forecast at different “quantiles”
Train with 2021/2022
Test with 2023

## Slide 39: Feature importance
Solar position
Deterministic forecast
Novel indicators

## Slide 40: Sample results

## Slide 41: Sample Results
2.5x

## Slide 42: Performance Statistics over 2023
PICP: Prediction Interval Coverage Probability
  What fraction of observations fall in a prediction interval, e.g., 95% P.I.?
PINAW: Prediction Interval Normalized Average Width
  Just because 95% of obs. fall in the 95% P.I. doesn’t mean it’s helpful…
Normalized to clear sky
“reliable”
“sharp”

## Slide 43: Comparison with Persistence Ensemble
Persistence Ensemble, PeEn: Like a historical PDF
(removed intervals where obs. was 0% of clear sky)

## Slide 44: Visual Comparison:
PeEn
ML

## Slide 45
Timeout!
Of course it’s better than persistence! How do you know it’s actually useful??
Great question! I don’t know that, but:
EPRI OPTSUN [1] showed potential for reliability improvements with no cost increase by using probabilistic forecasts
These forecasts appear to be better than the ones used for Southern’s system in OPTSUN
These forecasts only get better with a better deterministic forecast
[1] https://www.epri.com/optsun, see W. Hobbs, “Probabilistic Methods in Operations”, ESIG 2022 Spring Workshop for my summary (recorded: https://www.youtube.com/watch?v=1aO4kOoR2nc&t=1370s)

## Slide 46: Operational Deployment Considerations
Runs in < 15 minutes on my 4-year-old laptop
Retraining with representative observations and deterministic forecasts
Account for changes over time: increasing sites, plant availability
Consider a reforecast (a.k.a., historical forecast, “hindcast”) from the deterministic forecast provider
Consider supplementing observations with satellite-based irradiance (plus power model) to build a longer history of newer fleet
Especially if you don’t want outages included in forecast uncertainty

## Slide 47: Areas for Future Work
Hyperparameter tuning
Shorter and longer forecast horizons (than day-ahead)
Extrapolation?
Improved features
Additional weather models
Ramp rate probability forecasts
Probabilistic net load

## Slide 48: Available Code
github.com/williamhobbs/solar-fleet-forecast-probability-tool
BSD-3-Clause License
Python, with Jupyter Notebooks to run everything yourself
Please let me know if you use it!

## Slide 49: Questions? whobbs@southernco.com
github.com/williamhobbs/solar-fleet-forecast-probability-tool

## Slide 50: Sample data
January

## Slide 51: Sample data
August

## Slide 52: Sample data
October

## Slide 53: Using this uncertainty information
Sometimes, there is a clear relationship between error and the GEFS ensemble spread (standard deviation of total cloud cover, or TCC):
(Jan. 2021)

## Slide 54: Using this uncertainty information
… but not always
(Apr. 2021)

## Slide 55: Quantiles
Quantile examples:
  0.5 is 50th percentile, or expected value
  0.95 is 95th percentile
  Can be used for prediction intervals, e.g., 0.95 and 0.05 bound the 90% prediction interval (expect actual to fall in that range 90% of time)